## Slide 1: CPU Garage Challenge My Solution & Thoughts
Amichai Ben-David

## Slide 2: Agenda
CPU-Challenge Preface
Naïve Solution
Coding Style
Pipe-Line
Multi-Issue
Integer Division Accelerator
Branch Prediction
L1 Instruction Cache
Performance analysis

## Slide 3: CPU-Challenge Preface
Implementing a "HACK computer“
Compete over best performance on a specific benchmark when loaded to an FPGA
The program has visual feedback that can be seen on a VGA connection from the FPGA.
Links: Hack computer - Wikipedia Home | nand2tetris
CPU-Challenge Preface

## Slide 4: Naïve Solution
Single issue
Minimal complexity
Multi-Cycle due to Synchronous memory - See “Stall” signal in RTL
Naïve Solution

## Slide 5: Coding Style
CamelCase
Coding
Style

## Slide 6: Coding Style
CamelCase
The use of “Macros” for sequential logic (Non blocking assignment)
`define MSFF(q,i,clk) \
always_ff @(posedge clk) \
q<=i;
`define EN_MSFF(q,i,clk,en) \
always_ff @(posedge clk) \
if(en) q<=i;
`define RST_MSFF(q,i,clk,rst) \
always_ff @(posedge clk) begin \
if (rst) q <='0; \
else q <= i; \
end
`define EN_RST_MSFF(q,i,clk,en,rst)\
always_ff @(posedge clk) \
if (rst) q <='0; \
else if(en) q <= i;
Coding
Style

## Slide 7: Coding Style
CamelCase
The use of “Macros” for sequential logic (Non blocking assignment)
Pipe Staging naming convention
// Sample Ctrl Bits 101 -> 102
`MSFF( SelImmAsAluOut102, SelImmAsAluOut101, Clock)
`MSFF( SelMorA102 , SelMorA101 , Clock)
`MSFF( CtrlAluOp102 , CtrlAluOp101 , Clock)
`RST_MSFF(SsHit102 , SsHit101 , Clock, Reset)
`RST_MSFF(D_WrEn102 , D_WrEn101 , Clock,(Reset || RstCtrlJmp103))
assign NextD_Data102 = AluData102;
//From Cycle 102 -> 101
`EN_MSFF( PreD_Data101, NextD_Data102, Clock, D_WrEn102)
`MSFF( D_Data102 , D_Data101 , Clock)
Coding
Style

## Slide 8: Coding Style
CamelCase
The use of “Macros” for sequential logic (Non blocking assignment)
Pipe Staging naming convention
The use of Structs & Enums
typedef enum logic [2:0] {
NO_JMP = 3'b000,
JGT = 3'b001,
JEG = 3'b010,
JGE = 3'b011,
JLT = 3'b100,
JNE = 3'b101,
JLE = 3'b110,
JMP = 3'b111
} t_jmp_cond ;
typedef enum logic {
A_TYPE = 1'b0,
C_TYPE = 1'b1
} t_inst_type;
always_comb begin
// (Inst101[0][15:13] == 3'b111) -> C_TYPE
InstType101 = (Inst101[0][15] == 1'b0) ? A_TYPE : C_TYPE;
M_WrEn101 = (InstType101 == C_TYPE) && Inst101[0][3];
D_WrEn101 = (InstType101 == C_TYPE) && Inst101[0][4];
A_WrEn101 = (InstType101 == C_TYPE) && Inst101[0][5];
Coding
Style

## Slide 9: Coding Style
CamelCase
The use of “Macros” for sequential logic (Non blocking assignment)
Pipe Staging naming convention
The use of Structs & Enums
Spaces -> Not TABS!!
Coding
Style

## Slide 10: Pipe-Line
Traditionally: Fetch -> Decode -> Execute -> Memory_Access -> Write_Back
Intel Design - https://youtu.be/o_WXTRS2qTY
Many complex dependency issues which are solved in a very complex Architecture
Pipe-Line

## Slide 11: Pipe-Line
Simple 5 Stage, single issue RISCV Design.
3 Types of Hazards:
  Data Hazard - Solved with Forwarding unit.
  Load Hazard - Solved with Bubble + Back pressure + Forwarding unit.
  Ctrl Hazard - Solved with Bubble + Back pressure + Pipe Flush.
Pipe-Line

## Slide 12: Pipe-Line
“RISC” type CPU & ISA use a “load/store” architecture Meaning, to do any arithmetic on Memory Data you must: 1) “Load” Data from memory to Register File 2) Instruct an ALU operation 3) “Store” Data back to Memory from register file
Hack:
1) Hack is not a traditional “RISC” machine 2) The Memory Address is determent in the A Register. 3) Load & Store operation use the Same A register to determine the Data Address 4) Can Read-Modify-Write in a single instruction
> M = D + M
Pipe-Line

## Slide 13: Pipe-Line
Need to support:
To execute these instruction in pipe-line fashion, need to have the “LOAD” execute speculatively for line (3) so the Data will be ready to enter ALU at line (4).
  1) A = 5 // Write immediate to A
  2) D = A // Save the Immediate to Register D
  3) A = 10 // Write Address to register A
  4) M = D + M // Calculate & Store: M[10] = 5 + M[10]
Pipe-Line

## Slide 14: Pipe-Line |My Solution:
Load the Data from memory at the “Decode”
Data is ready for “Execute”.
Clear split of Data Path signals vs Control Signals.
Pipe-Line

## Slide 15: Pipe-Line |My Solution:
Memory must support Dual Read & single Write in same cycle. (Decode, Write_Back, VGA)
We are limited to the FGPA standard memory types (which is at most dual port memory)
Dual Read & single Write is achieved by duplicating the D_MEM.
Pipe-Line

## Slide 16: Multi-Issue
Simple dual issue:
Fetching 2 instructions from the ROM, we can decode them as a single entity and execute them together. This is known as fusion"fusion“
loading an immediate to register D:
loading from memory in a specific location to register D:
Storing to memory in a specific location the data of register D:
  > @5 > D = A // D = 5
  > @5
  > D = M // D = M[5]
> @5 > M = D // M[5] = D
Multi-Issue

## Slide 17: Multi-Issue
To support a multi-issue design, Fetch multiple Instruction per cycle.
Instantiate the Instruction memory multiple times and Fetch Subsequent 20 instruction. This is done using a “generate for”.
Multi-Issue

## Slide 18: Multi-Issue
Dual Issue: Decode logic will Set the correct Ctrl bits for the Data Path
Multi-Issue

## Slide 19: Multi-Issue
8 Multi-Issue instruction fusion into a single operation
10 Multi-Issue instruction fusion into a single operation
Ctrl Signals:
Dedicated HW for the fusion instructions
Multi-Issue

## Slide 20: Multi-Issue
The program Counter needs to be incremented according to the decode Stage results:
The Instructions we decode are according to the new PC offset:
Multi-Issue

## Slide 21: Integer Division Accelerator
The Benchmark inner loop sequence of division:
Set M[1] to initial Value 0 (“Quotient”)
Set M[2] to initial Value 20,000 (“Dividend”)
Set M[3] to initial Value 10 (“Divisor”)
Start loop: Count # of Subtractions of Dividend from Divisor are larger than 0.
  M[1] = M[1]++ // Quotient++
  M[2] = M[2]-M[3] // Dividend – Divisor
  If(M[2] >0) Jump to @LOOP
End of loop – M[1] has the final “Quotient” 0f M[2]/M[3]
M[1] = 0
M[2] = 20,000
M[3] = 10
(LOOP)
M[1] = M[1] +1
M[2] = M[2] – M[3]
If(M[2]>0)
jump @LOOP
Integer Division Accelerator

## Slide 22: Integer Division Accelerator
Detect the division LOOP using a “shift register” History buffer
Split the Match into 2 Cycles to ease the timing converges on the match logic
Integer Division Accelerator

## Slide 23: Integer Division Accelerator
HW Division module Instance:
Integer Division Accelerator

## Slide 24: Integer Division Accelerator
HW Division module Content:
(170) 13-1. Improving the Division Hardware - YouTube
Integer Division Accelerator

## Slide 25: Branch Prediction
Incase of Control Hazard, the pipe Needs to be flushed, and the PC will be updated accordingly.
Option 1: Insert 2 NOPs before setting the correct NextPC. This will make sure only correct commands will be executed.
Option 2: “Always Not Taken” – Keep fetching speculatively PC +1. only incase of ‘branch taken’ flush the Pipe and fetch correct instruction.
Option 3: “Always Taken” – Every Decode with potential branch, branch. Incase of wrong branch, flush and return to PC+1.
Option 4: Design a Branch predictor that can count the number of iteration a specific loop needs until branch not taken.
Branch Prediction

## Slide 26: L1 Instruction Cache - Instruction Queue
L1 Instruction Cache
Add a ~30 Instruction deep instruction queue
Prefetch ~10 instructions every cycle.
Queue in Register Style - Allow multiple combinatorial reads from any entry in queue.
Fitch & Decode in a single Cycle. (combinatorial Fitch read) - Update Next PC more simply (multi-issue decode)
Instruction Queue deep enough to allow the critical loop to Brach without the need to fetch the instruction again.
Incase of branch that is not in L1 Cache

## Slide 27: Performance analysis
Out of the Box:
  30,000 – # of LIP. Each is ~150 instructions + inner Loop
  2,000 – # of LOOPs. Each is 12 instructions
  Total:
  30,000 x (2,000 x 12 + 150) = 724,350,000 -> ~14 sec.
  The “Naïve solution” was a 2 Cycle per instruction (without Pipe- line).
  As expected, we Got ~28 Sec
Performance analysis

## Slide 28: Performance analysis
Pipe-line
  30,000 – # of LIP. Each is ~150 instructions + inner Loop
  2,000 – # of LOOPs. Each is 12 instructions + 2 for the pipe flush
  Total:
  30,000 x (2,000 x (12+2) + (150+2)) = 724,350,000 -> ~16 sec.
Performance analysis

## Slide 29: Performance analysis
Dual-Issue
  30,000 – # of LIP. Each is ~150 instructions + inner Loop
  2,000 – # of LOOPs. Each is 12 instructions + 2 for the pipe flush
  Total:
  30,000 x (2,000 x (12/2+2) + (150/2+2)) = 482310000 -> ~9.6 sec.
Performance analysis

## Slide 30: Performance analysis
Multi-Issue
  30,000 – # of LIP. Each is ~150 instructions + inner Loop
  2,000 – # of LOOPs. Each is 12 instructions + 2 for the pipe flush
  Total:
  30,000 x (2,000 x (12/4+2) + (150/7+2)) = 301,185,000 -> ~6 sec.
Performance analysis
Average

## Slide 31: Performance analysis
Instruction queue + Branch always Taken:
  30,000 – # of LIP. Each is ~150 instructions + inner Loop
  2,000 – # of LOOPs. Each is 12 instructions + 2 for the pipe flush
  Total:
  30,000 x (2,000 x (12/4 +2) + (150/7 +2)) = 181,125,000 -> ~3.6 sec.
Performance analysis
Average

## Slide 32: Performance analysis
HW devider:
  30,000 – # of LIP. Each is ~150 instructions + inner Loop
  2,000 – # of LOOPs. Each is 12 instructions + 2 for the pipe flush
  12 + 17 Instruction for the HW devider
  Total:
  30,000 x ( (12 + 18) + (150/7)) = 1542857 -> ~0.03 sec.
Performance analysis
Detect Division is needed
Perform 16-bit Division

## Slide 33: Questions